## Slide 1
Groundwater & Surface Water Data Management
MMG Rosebery Mine, Tasmania
Tom Wilson (EScIS) & Joe Kwan (MMG)

## Slide 2: Presentation Overview
  Mine Operations
  Site hydrology & hydrogeology
  Why monitor?
  Monitoring program
  Monitoring event plan  field data capture  review
  Lab data receipt, validation & data analysis
  Data outputs/reporting & sharing of data
  Benefits of the EScIS system at MMG

## Slide 3
Rosebery Location

## Slide 4: Rosebery Operations
  Underground poly-metallic base metal mine
  Commenced 1936, mine life to 2024
  Open stopes extract ore from up to 1500m depth
  Ore trucked to surface for crushing & processing

## Slide 5: Rosebery Operations
  Produces zinc, lead, copper concentrates & gold doré
  Gold recovered by gravity, remainder by froth floatation
  Concentrates shipped to Nyrstar (Hobart & Port Pirie)
  Gold shipped to Perth

## Slide 6: Hydrology & Hydrogeology*
  Sulphide deposit within Cambrian Mount Read Volcanics
  Mine data indicates:
    top 100m = increased permeability (weathering);
    shear zones and faults = increased permeability;
    below 100m, uniform permeability decrease with depth
  Groundwater flow system typified by a deep fractured aquifer (containing the mine voids), overlain by surficial glacial deposits & weathered material
  *LR Evans 2009

## Slide 7: Hydrology & Hydrogeology
  Significant SW/GW interaction throughout catchment
  Regional rainfall >> evapotranspiration (dense vegetation)
  Catchment water budget:
  42% (of precipitation) runs off as surface water flow
  24% lost to evapotranspiration
  17% becomes groundwater, discharged as baseflow into creeks & rivers within the catchment
  18% remains as groundwater discharge beyond the catchment
  Mined materials are potential sources of Acid Mine Drainage:
  tailings dams waste rock mine workings

## Slide 8: Hydrology & Hydrogeology
  3D model suggests the potential area for mine contaminated groundwater discharge is far more limited than was previously believed by mine operators

## Slide 9: Hydrology & Hydrogeology
  Understanding the areas of potential impact:
  focusses monitoring point distribution
  focusses future modelling efforts
  Background monitoring used to test the model & provide data for future model calibration/validation
  Thus the quality and validity of monitoring is critical to ongoing operations and mine closure plan
  i.e. garbage in = garbage out

## Slide 10: Environmental Protection Notice
  EPN specifies sample locations, frequency & analysis (informed by model)
  Primarily to monitor potential AMD impacts
  Broad range of WQ parameters & analytes
  pH, EC, TDS
  Fe, Mn, Zn, Ni, Cu, Pb, Cd, As, Hg, Al
  Nitrate, TN, TP, SO4, Ca, Mg
  Acidity & alkalinity
  TPH, BTEX

## Slide 11: Water Monitoring Program
  10 SW sites  weekly
  20 SW sites  monthly
  40 SW sites  quarterly
  50 GW bores monitored bi-annually (wet & dry seasons)
  Field parameters + laboratory analysis
  (also 13 dust gauges, 8 Hi-Vol air samplers, plus continuous noise, vibration & meteorological loggers)
  Result  Large volumes of field, lab (& logger) data

## Slide 12: EDMS
  MMG have the EScIS Environmental Data Management System
  Operates from a central SQL server database (DB)
  DB hosted on-site server
  Three integrated ‘off-the-shelf’ applications:
  LSPECS Field event planning, PM & validation
  pLog Field data capture
  ESdat Analysis, interpretation, outputs
  All applications talk to the one SQL DB

## Slide 13: LSPECS
  Key functions:
    Field program design/planning & delegation
    Field program tracking (all projects, auto-create repeat events)
    Review/validation of field & lab results
  Web browser interface – intuitive design
  Import all laboratory details (quotes, sample bottles etc.)
  Design a complete SAQP (QA samples, field readings, docs etc.)
  Assign trigger criteria (published or derived)

## Slide 14: Monitoring Round - Plan

## Slide 15: pLog
  Android or windows tablet software
  LSPECS sample plan ‘synced’ to pLog tablet over cloud (3-4G/wifi)
  Full electronic data capture on one device:
Field parameters & sample information
Geological bore logs
Photos (geotagged)
GPS locations (new sample points, find existing)
  pLog will operate online or offline – works remotely
  Captures planned or ad-hoc data

## Slide 24
SRN
From LSPECS review field data Submit lab analysis
LSPECS/pLog Workflow
Review & approve lab analysis
Detailed analysis in ESdat
Create sampling plan
from LSPECS in office
Conduct sampling & collect field/sample data
Data synced back to LSPECS
Sync via cloud to pLog
installed on tablet

## Slide 25
LSPECS
  Sync completed round from pLog back to LSPECS (via cloud)
  In LSPECS:
  Review field data
  Review lab analysis request (new/missing samples?)
  Submit analysis request electronically to lab (into LIMS)
  Receive electronic SRN (auto check TAT)

## Slide 26: Lab Submissions

## Slide 27
LSPECS – lab analysis data review
  Receive lab results in ESdat format – auto upload
  Auto comparison with trigger criteria
  Immediate (email) notification (customisable)
  Review data quality
  Attach QA commentary to analysis (shared amongst team)
  Run full field & lab QA (RPDs, TBs, LCS, MB etc)
  If acceptable, approve event & data for ESdat analysis

## Slide 28: Tabulated Lab Results

## Slide 29
Benefits of LSPECS/pLog at MMG
  Centralised data storage & project management
  Easy creation of field events & resource management
  Auto-scheduling of events = no missed rounds or scope errors
  No field data sheets = no manual transcription saves time & reduces errors
  Validation processes = confidence in achieving DQOs
  Auto notification of issues (e.g. exceedence, QA) = rapid response

## Slide 30
ESdat
  LSPECS approved data becomes available for analysis in ESdat
  ESdat desktop software – specifically designed interface
  Manages many data types in one SQL dbase, including:
  Coordinates (for mapping) Chemistry (any matrix)
  SW Flow data Water levels
  Well construction Geology
  Env. standards/criteria Emissions (dust, noise)

## Slide 31
Powerful ESdat Features
  Easily combine data types via queries:
  e.g. Coordinates + Chemistry  interrogate via internal GIS
  Create, save and re-use complex data filters
  Quickly isolate data subset of interest
  Stop using Excel!
  Export directly to third party software from one DB
  Formatted tables & graphs, ProUCL, Piper/Schoeller diags
  gINT/Winlog ArcGIS/Mapinfo/Google Earth/Surfer/CAD
  e.g. Coordinates + Water levels  Surfer for contours

## Slide 32
Benefits of ESdat at MMG
  Seamless integration of new data with historical data
  Monitor long term trends (auto update existing graphs)
  Easily create scheduled/ad-hoc outputs for EPA in required format
  Incident response – data is readily available
  Quickly generate outputs to suit external consultants
  Reporting (share data in ESdat format or Excel tables)
  Modelling (Excel & pivot tables)
  Easy transition as staff come & go (no unsupported customisations)

## Slide 33
Future MMG EDMS expansion
  Implementation of the EDMS = step change in operations
  This change needs to be managed with a long term view
  Application of suitable EDMS features = real productivity increase
  Less time managing data = more interpretation time
  = better science (& less risk)
  MMG looking to expand use of EDMS to other data types:
  Terrestrial (biological) monitoring
  Aquatic monitoring

## Slide 34
Acknowledgements
  Groundwaters in wet, temperate, mountainous, sulphide-mining districts: delineation of modern fluid flow and predictive modelling for mine closure (Rosebery, Tasmania)
  Lee R. Evans, PhD thesis, UTas, 2009

## Slide 35
  Thank you
  www.esdat.com.au